## Slide 1: VLBI astrometry: IAA CRF solution
S. Kurdubov,
E. Skurihina, S. Mironova
Institute of Applied Astronomy RAS

## Slide 2: IAA CRF activity
Global VLBI data processing for source positions
Optimal defining sources selection
Systematic differences between CRF realizations
Galactic aberration
Source positions time series
QUASAR VLBI data processing software

## Slide 3: QUASAR features
Reduction parameteres
  Most calculations done according to the IERS Conventions (2003)
  Various options
Single and multi session estimations
Estimation options
  Various parameters can be estimated
  Every parameters can be global, arc or stochastic
  Every parameters can be estimated as polynomial trends
Least Square Collocation method
  Mean correlation function
  Individual variance values for each station

## Slide 4: Global Solution Parameters
Global:
  RA, DE
  Stations coordinate and velocities
  Antenna offset
  Galactic aberration parameters
Arc
  Earth orientation parameters (Xp,Yp,UT1-UTC,Xc,Yc)
  Linear trend of wet zenith delay
  Troposphere gradient east and north
  Quadratic trend of station clock offset
Stochastic
  Stochastic component of WZD
  Stochastic component of clock offsets

## Slide 5: Constraints
no-net-rotation for 212 defining sources ICRF1
no-net-rotation/translation for positions and velocities of 15 stations (BR-VLBA , FD-VLBA , FORTLEZA, HN-VLBA , KP-VLBA , LA-VLBA , MATERA , NL-VLBA , ALGOPARK, WESTFORD, WETTZELL, HARTRAO , KOKEE , NYALES20, ONSALA60)
Not estimated sources observed less than 15 times and stations velocities of less than one year observation period (soft constraints)
Sum of clock offsets is equal to zero in one session
Soft constraint for EOP for sessions with low geometry
Equal stations velocities for stations on same site

## Slide 6: Optimal defining sources selection
Given catalogue RA, DE, arbitrary catalogue ra, de.
Rigid rotation transformation model
Geometry part
Inaccuracy of positions part
Least Square for A1, A2, A3 estimation

## Slide 7
IAA core sets in comparison with the OPA set

## Slide 8
Estimation of Solar system acceleration from VLBI
Calculation was performed by the global adjustment of the VLBI data
The estimated value of acceleration vector a=(4.7±0.5) ∙10ˉ¹° м/c², α=288°±5°, δ=0°±5° significantly differs from the theoretical one but comparable with the other results.
Results presented at 20th EVGA Meeting & 12th Analysis Workshop, March 29 - 31, 2011

## Slide 9: IAA global solution for ICRF2
4404 VLBI sessions
Aug 1979 - Jan 2011
6721880 delays
132 stations (15 with discontinuous motion)
3493 radio sources

## Slide 10
Сист. ошибки ICRF2(752) Δ δ, в мксд

## Slide 11
Смещения источника 0923+392 по α

## Slide 12
Source positions formal errors vs number of observations chart

## Slide 13
Source positions formal errors vs number of observations chart

## Slide 14
 | Mean Sigma, mas | WRMS vs ICRF2, mas
RA | 0.2 | 0.05
DE | 0.2 | 0.07
Comparison of CRF catalogue with the ICRF2

## Slide 15: International VLBI Service web site
http://ivscc.gsfc.nasa.gov/products-data/products.html
ftp://ivs.bkg.bund.de/pub/vlbi/ivsproducts/trf/iaa2011a.trf.gz
ftp://ivs.bkg.bund.de/pub/vlbi/ivsproducts/trf/iaa2011a.crf
iaa2009b
iaa2008b
iaa2007b

## Slide 16: Скорости движения источников
Источник | К-во набл. | Эпоха | Положение(мсд) |  |  |  | Тренд (мсд/(10 лет)) |  |  | 
 |  |  | R0 | SR0 | D0 | SD0 | R1 | SR1 | D1 | SD1
0059+581 0336-019 0458-020 0528+134 0552+398 0851+202 0923+392 1228+126 1308+326 1404+286 1638+398 1739+522 1741-038 1807+698 2037+511 2121+053 2145+067 2200+420 2201+315 2223-052 | 1370 961 834 1243 2102 1669 1865 689 1087 751 765 1323 1597 718 1000 504 1049 538 518 714 | 2002.6 2002.8 2000.4 1998.1 1997.7 1998.8 1997.1 2002.8 1998.2 1998.3 2000.4 1999.8 2000.9 2004.8 2004.9 1999.6 1997.9 1992.4 2000.7 2003.8 | -.025 -.020 -.007 -.008 -.002 .003 .019 .006 .022 .002 .003 .006 .009 -.005 -.002 .007 -.009 .004 .009 -.016 | .001 .004 .003 .003 .001 .002 .002 .005 .003 .003 .002 .002 .002 .005 .004 .007 .003 .003 .005 .004 | -.022 .007 -.004 .012 .014 .010 .014 .004 .027 .047 .024 -.004 -.003 -.010 -.008 -.002 .013 .026 .055 -.028 | .002 .004 .004 .003 .001 .002 .002 .006 .003 .005 .003 .002 .002 .005 .005 .005 .003 .005 .007 .006 | .009 -.001 -.068 -.003 -.005 -.022 .131 -.006 .060 .032 -.018 -.015 -.015 .016 -.006 .066 -.083 -.065 -.011 .038 | .003 .007 .007 .006 .002 .003 .003 .010 .006 .005 .006 .003 .003 .007 .005 .012 .007 .005 .012 .009 | -.021 -.022 -.023 .028 -.014 .041 -.041 -.017 .017 .063 -.002 .011 .013 .000 .039 -.027 .056 -.049 .018 .047 | .003 .007 .007 .006 .002 .003 .003 .011 .008 .009 .007 .004 .004 .007 .006 .008 .006 .011 .016 .010